## Slide 1
Using Airborne LiDAR for Golden-winged Warbler Management
2013 WVAGP Annual Meeting
Stonewall Resort State Park
Sam Lammie, GISP
slammie@fs.fed.us
Geographer
Monongahela National Forest
200 Sycamore Street
Elkins, West Virginia 26241
Photo credit: Liz Stout
Photo credit: Kyle Aldinger

## Slide 2
Airborne LiDAR
Using Airborne LiDAR for Golden-winged Warbler Management
By measuring the time it takes light to bounce off an object, and knowing the speed of light (186,000 miles per second), one can detect the distance of the object.
Airborne LiDAR – using 1064-nanometer laser beams
Bathymetric LiDAR Systems – using 532-nanometer laser beams
(Source: ESRI)
“It's faster than a speeding bullet. It can measure buildings in a single pulse.” (GCN, 2013)
Challenge is in firing rapid pulses of light (up 150,000 per second)

## Slide 3
Background
The Golden-winged Warbler is one of the most critically threatened, non-federally listed species in eastern North America.
The rate of population decline has accelerated in the past decade, with the most precipitous declines in the Appalachian region, particularly West Virginia.
Because a variety of habitats are used by Golden-winged Warblers, they can be used as an umbrella species to address the needs of other species that require a range of early successional habitats.
Source: Wikipedia

## Slide 4
LiDAR shedding new light on habitat characterization and modeling
(Vierling, et al, 2008)
The three-dimensional arrangement of habitat is fundamental to how animals interact with the environment
LiDAR remote sensing is a tool that can characterize three-dimensional habitat structure of terrestrial and aquatic environments in fine detail across broad areas
LiDAR data may replace many labor-intensive, field-based measurements, and can characterize habitat in novel ways
Incorporating LiDAR data into studies of animal–habitat relationships will help to improve models used for species management and conservation.

## Slide 5
Purpose
Using LIDAR to analyze habitat
structure, both vertically and
horizontally, may be the best option
for measuring habitat complexity
at the appropriate scale.
Standard remote sensing products, using satellite imagery and/or digital aerial photography, provide critical horizontally-dependent, information on vegetation, but are not suitable for mapping vertical structure – a critical habitat component for this species.
Source: Kyle Aldinger (PhD candidate, WVU) and Cathy Johnson (Wildlife Biologist, MNF)
“Hardly every see them unless you hear them first”
Early successional state – complicated structure
Golden-winged Warbler Working Group (2009)

## Slide 6
Gay Sharp/Hoover range allotments
550 acres
elevations ranging from 3,000 – 4,000 ft
Study area

## Slide 7
Gay Sharp/Hoover range allotments
550 acres
elevations ranging from 3,000 – 4,000 ft
LiDAR data details
Collected by WVU NRAC (June, 2012)
Piper Navajo flown at approximately 2000-ft AGL at an
  average speed of 135 knots
Collected with the following parameters:
  Pulse Rate Frequency of 100,000 Hz
  Scan Frequency of 54 Hz
  Scan Angle of 24 degrees (full Field of View (FOV))
WVU NRAC post-processed the data and a ground model
  was derived from the LiDAR dataset
Deliverables included LiDAR LAS 1.2 files (grouped in ASPRS classes):
  Class 1 default
  Class 2 ground
  Class 3 low veg (<1m)
  Class 4 medium veg (1-3m)
  Class 5 high veg >3m, and
  Bare Earth only LiDAR LAS 1.2 files (Class 2)
  Latest LiDAR exchange LAS format is 1.4 (approved 11/11)

## Slide 8
First return
Second return
Third return
Last return
LiDAR Returns

## Slide 9
DEM
DSM
Digital surface model (DSM)
Digital elevation model (DEM)
Digital Models

## Slide 10
ArcGIS 10.1 and LiDAR
.las Files
In ArcGIS 10.1, ESRI introduced LAS files, a new dataset type, which is a pointer type to collections of LAS files (or tiles) and allows you to display point clouds or surfaces (in 2 or 3D), run statistics, and even edit the point clouds.

## Slide 11
Building the LAS Dataset
54,000,000

## Slide 12
Generating Statistics

## Slide 13
LiDAR LAS dataset
New file type
File-based
Stores references to LAS files on disk
Can reference breakline data
Treats a collection of LAS files as one logical dataset
Prefer to organize as tiles for these massive point cloud datasets, but there are several data types available for working with LiDAR data including:
  Terrain
    Introduced in ArcGIS 9.2
    Multi-resolution TIN service model
    Long-term solution for LiDAR projects/surveys
  Mosaic
    Introduced in ArcGIS 10.0, enhanced in 10.1
    Catalog, process, visualize, and share imagery and LiDAR
  LAS
    Introduced at ArcGIS 10.1
(Source: ESRI)
Direct access to data
File cataloging
View data as pts/TINs
Statistics, QA/QC
Filter/query
Profile and 3D views
File editing
Add/edit constraints
Advantages:

## Slide 14
LAS Dataset toolbar

## Slide 15
Elevation Class Return
LAS dataset rendered as points:
LAS dataset rendered as a triangulated surface:
Elevation Slope Contour

## Slide 16
Generating an intensity image
  Define a point filter for first returns
  Run LAS dataset to Raster tool
Cell size 2 to 4 times point spacing
Source: ESRI

## Slide 17
  Intensity image is used as an aid in feature detection and extraction, in lidar point classification, and as a substitute for aerial imagery when none is available.

## Slide 18
Editing LiDAR data
LAS point clouds can be profiled, displayed and edited
Surface constraints can be added or removed

## Slide 19
LiDAR 1.2 spec

## Slide 22
Filtering point cloud for display

## Slide 23
Low Vegetation
Medium Vegetation
High Vegetation
(<1 meter)
(1 – 3 m)
(>3 m)
Ground
Point clouds over DSM

## Slide 24
Point cloud shown in ArcScene by classification codes

## Slide 25
GWWA nest locations
ArcScene

## Slide 26
ArcScene
GWWA nest locations
GWWA territories
Profile

## Slide 27
(<1 meter)
(1 – 3 m)
(>3 m)

## Slide 28
Other Resources
Free software
  Fusion Version 3.21 (October, 2012 build)
  FugroViewer Version 1.52
Intergraph (ERDAS) Imagine
QCoherent’s LP360
Videos
  YouTube videos
  ESRI training videos
  (two free 60 minute videos)

## Slide 29
Current WV LiDAR Coverage
2013 WVAGP Annual Meeting
Stonewall Resort State Park
Sam Lammie
Geographer
Monongahela National Forest
200 Sycamore Street
Elkins, West Virginia 26241