## Slide 1: Stormwater and GIS
Eastern Panhandle WV GIS User Group Meeting
September 2, 2015
Jennifer Klages - Jennifer.L.Klages@wv.gov
Sebastian Donner - Sebastian.Donner@wv.gov
WV Department of Environmental Protection
Watershed Improvement Branch

## Slide 2: GIS & STORMWATER
Municipal Separate Storm Sewer System - MS4 permit requirements
Construction Stormwater permit
Ordinance compliance
Flood plain management
Land use development
Chesapeake Bay TMDL
TMDL - Total Maximum Daily Load - West Virginia TMDLs @
http://www.dep.wv.gov/WWE/watershed/TMDL/Pages/default.aspx

## Slide 3: MS4 – Regulatory Stormwater GIS Frontier
Municipal - Local Government Separate - Separated from Sanitary Sewer Storm - Rain Causing Runoff Sewer – Conveyance System - Structural

## Slide 6: Water Quality Standards
Designated uses = Desired uses
Drinking, Agriculture, Industrial water supply
Human Contact Recreation
Catching/eating Fish
Aquatic life protection
Religious/cultural practices
water.epa.gov/learn/training/wacademy/archives.cfm#w20120321

## Slide 7: Stormwater Runoff
Precipitation flowing over land
Increased by impervious surfaces
  Urban development
  Hard – concrete, asphalt, roofs
  No infiltration
Collects pollutants
  Sediments
  Debris
  Chemicals
    Nutrients
    Heavy metals
    Hydrocarbons
    Endocrine disruptors
Typically not treated
Notes: http://cfpub.epa.gov/npdes/home.cfm?program_id=6

## Slide 9: Watershed Protection Elements
1. Minimize impervious surfaces
2. Preserve, protect, create and restore ecologically sensitive areas
3. Prevent or reduce thermal impacts to streams
4. Avoid or prevent changes to streams and other bodies of water
5. Protect trees and other vegetation
6. Protect native soils

## Slide 13: Preserve and Protect
Undisturbed Natural Areas
Ecologically Sensitive Areas
Natural Drainage Features
Porous, Erodible, and Native Soils
Valuable Habitat Areas
Trees and Vegetation
Riparian Buffer
Steep Slopes

## Slide 19: Incorporate
Landscaping Areas in Parking Lots
Alternative Culs-de-Sac
Shared driveways
Sidewalks on one side for low-traffic roads
Grass swales used in lieu of curb & gutter
Designs that Reduce Hydromodification and Stream Impacts

## Slide 21: Reduce
Impervious Surfaces
Clearing and Grading Limits
Setbacks and Frontages
Roadway Lengths and Widths
Sidewalk and Driveway Lengths and Widths
Parking Lot Footprints
Building Footprints

## Slide 22: Compensate
Implement Stormwater Control Measures, aka structural
Best Management Practices (BMPs)
Sheet Flow to Vegetated Filter Strips and Conservation Areas
Regenerative Stormwater Conveyance System
Impervious Surface Disconnection
Bioretention
Infiltration
Filtration
Permeable Pavement
Grass Swale
Rainwater Harvesting
Vegetated Roofs
Stormwater Wetlands

## Slide 23: Essential Smart Growth Fixes for Rural Planning, Zoning, and Development Codes
http://www.dep.wv.gov/WWE/Programs/stormwater/MS4/permits/Documents/Essential_Smart_Growth_Fixes_Rural_Development_%202012.pdf
Determine Areas for Growth and for Preservation
Incorporate Fiscal Impact Analysis in Development Reviews
Reform Rural Planned Unit Developments
Use Wastewater Infrastructure Practices That Meet Development Goals
Right-Size Rural Roads
Encourage Appropriate Densities on the Periphery
Use Cluster Development to Transition From Town to Countryside
Create Annexation Policies and Development Standards That
Preserve Rural Character
Protect Agricultural and Sensitive Natural Areas
Plan and Encourage Rural Commercial Development

## Slide 24: Community Culture and the Environment
Comprehensive EPA guide with case studies
http://www.epa.gov/care/library/community_culture.pdf

## Slide 25: How To Keep Track? - GIS
http://tagis.dep.wv.gov/WVWaterPlan

## Slide 26: BMP Tracking & Reporting
MS4 permit and Chesapeake Bay
1. Project type/category (new/re development, retrofit)
2. BMP name(s)
3. Stormwater Treatment or Runoff Reduction
4. Volume of water treated at a site
5. Impervious acres treated by the practice(s)
6. Total site acres treated by the practice(s)
7. Location (lat/long)
8. Date installed
9. Date inspected
10. Practice duration

## Slide 28: Land Use Change Verification
Land use changes 2011 through 2014
Chesapeake Bay Watershed
    Eight County Eastern Panhandle
Assessment of changes in nutrient & sediment loads due to development
“Holding the Line” to avoid net increases in the urban/developed lands sector

## Slide 29: Observed Land Use Changes
 |  | Total | Berkeley | Grant | Hampshire | Hardy | Jefferson | Mineral | Morgan | Pendelton
Permitted Acres |  | 5621 | 2464 | 833 | 58 | 158 | 1737 | 270 | 53 | 49
Land use change acres |  | 4190 | 1775 | 797 | 17 | 44 | 1370 | 159 | 18 | 10
% Permit Acres developed |  | 75% | 72% | 96% | 29% | 28% | 79% | 59% | 34% | 20%
% Permit Acres not used |  | 25% | 28% | 4% | 71% | 72% | 21% | 41% | 66% | 80%
% of TOTAL Land Use Changes |  | 100% | 42% | 19% | 0.4% | 1.1% | 33% | 4% | 0.4% | 0.2%
Preliminary Results

## Slide 30
TOTAL Land Use Change Summary |  |  |  | Percent of |  |  |  | 
Land Use | Acres |  |  | Total Land Use Change |  | Change in Delivered Loads (lbs/year) |  | 
 | PRE | POST | Δ Acre | PRE | POST | TN | TP | TSS
rid | 125 | 393 | 268 | 3.0% | 9.4% | 1,873 | 244 | 112
nid | 94 | 351 | 257 | 2.2% | 8.4% | 1,389 | 233 | 107
rpd | 390 | 944 | 554 | 9.3% | 22.5% | 3,091 | 143 | 32
npd | 319 | 652 | 333 | 7.6% | 15.6% | 2,450 | 121 | 27
rcn | 440 | 58 | (382) | 10.5% | 1.4% | (4,610) | (1,580) | (2,933)
hay | 71 | 54 | (17) | 1.7% | 1.3% | (54) | (5) | (1)
row | 1,236 | 63 | (1,173) | 29.5% | 1.5% | (28,785) | (1,378) | (173)
pas | 55 | 8 | (47) | 1.3% | 0.2% | (74) | (15) | (9)
trp | 4 | - | (4) | 0.1% | 0.0% | (222) | (36) | (13)
urs | 2 | - | (2) | 0.0% | 0.0% | (288) | (80) | (3)
for | 990 | 702 | (289) | 23.6% | 16.8% | (383) | (27) | (6)
hyo | 375 | 966 | 591 | 8.9% | 23.1% | 1,773 | 21 | 29
hvf | 90 | - | (90) | 2.1% | 0.0% | (810) | (34) | (13)
TOTAL LUC | 4,190 | 4,190 | (0) | 100% | 100% | (24,650) | (2,393) | (2,844)

## Slide 31: WV BMP Guidance Manual
http://www.dep.wv.gov/WWE/Programs/stormwater/MS4/Pages/StormwaterManagementDesignandGuidanceManual.aspx
www.dep.wv.gov
Water & Waste
– Permitting
– Stormwater
Permits
West Virginia Stormwater Management and Design Guidance Manual

## Slide 32
http://www.dep.wv.gov/WWE/Programs/stormwater/MS4/permits/Pages/ToolsandGuidance.aspx

## Slide 33: Erosion & Sediment Control https://apps.dep.wv.gov/dwwm/stormwater/BMP/index.html

## Slide 34: US Geological Survey
http://water.usgs.gov/edu/

## Slide 35: LID "Barrier Busters" Fact Sheet Series
http://water.epa.gov/polwaste/green/bbfs.cfm

## Slide 36: Bay Resources
Chesapeake Bay Program
www.chesapeakebay.net
Chesapeake Stormwater Network
www.chesapeakestormwater.net
Center for Watershed Protection
www.cwp.org
www.youtube.com/user/CenterforWatershed/videos
Watershed Implementation Tools
http://www.chesapeakebay.net/about/programs/watershed_implementation_plan_tools